MUXX memory management
# General principles
MUXX requires a memory mapped PDP-11 system to work. The system provides each task with a private virtual address space, nominally of up to 64KB. However, the 8 upper KB of the address space are reserved to map the UNIBUS IO space, so it is not available for user mode tasks[1]. Those upper 8KB are protected from access in user mode, and fully mapped and accessible under kernel mode (MUXX does not use supervisor mode).
[1] That 8 upper KB could be mapped into an arbitrary 8KB block of physical memory, but it would introduce some interesting problems if a process tries to invoke a system call passing a parameter resident in that memory block, so we will not implement that possibility in this MUXX version.
The PDP11 memory management unit provides 8 Page Address Registers to configure the memory mapping. Each of those 8 PARs can map up to 8 kilobytes of virtual memory. Please note that at this point MUXX does not use I/D space separation, so code and data share the same 64KB virtual address space. Each address space will make use of the 8 PARs to build its memory map:

PAR	Address	Content	Access
0	000000-017777	Vector table, kernel code and data	U: RO / K: RW
1	020000-037777	Kernel code and data	U: RO / K: RW
2	040000-057777	User code and static data	U,K:RW
3	060000-077777	User code and static data	U,K:RW
4	100000-117777*	User heap data	U,K:RW
5	120000-137777*	User heap/stack data	U,K:RW
6	140000-157777	Kernel/User stack data	U,K:RW
7	160000-177777	IO space	U:None / K:RW

The blocks marked with an asterisk are not allocated at process creation time. Those PARs are marked as “unmapped”, and are allocated if necessary. The upper block (just below the IOSPACE) will contain both the kernel and user stacks. The kernel stack will be located at the top of that bloc, and its size will be configurable using a muxxdef.h #define. The user stack will go just below the end of the kernel stack. A kernel stack underflow will (if stack underflow detection has been compiled in) will cause a kernel panic and will crash the system.
# Physical memory management
MUXX will run in a PDP-11 configured with 256KB of memory. It uses 18 bit addressing, so it will not make use of the rest of a bigger memory configuration. After acquiring experience running the MMU in 18 bit mode, an extension to use 22 bits will be considered. But not at this time.
That 256KB space will be divided in 128 chunks of 2KB (1KW). That chunk will be the low-level memory allocation unit. 2KB = 32d (40o) 64 byte blocks (the 64 byte block is the MMU allocation unit). To manage those chunks we will use a linked list of Memory Management Control Blocks (MMCBs), with the following structure:

Offset	Type	Name	Content
0	WORD	blockAddr	Number of block (physical address divided by 2048)
2	WORD	blockSize	Size (number of chunks)
4	WORD	ownerPid	Owning PID
6	WORD	ownerPAR	Mapping PAR
8	POINTER	nextBlock	Pointer to next block in the chain
10	POINTER	prevBlock	Pointer to previous block in the chain
12	WORD[2]	filler	Unused

Each MMCB will describe a block of memory, free or allocated to a process. If the ownerPid field of the MMCB is zero the block will be considered as free.
# System startup and process creation
At system startup MUXX will configure the MMCB list as follows:
- It will map PARs 0,1, and 6 to the first available 24KB of physical memory (8 KB per PAR), and will create the first three MMCBs as owned by the startup process (pid 1).
- It will create a free block MMCB for the rest of the physical memory.