MUXX Calling standard

This text documents the stack frame formats for the different types of call/transfer of control supported and managed by MUXX.
# General principles
- The hardware stack (pointed by the R6/SP register) will be used to hold saved registers and temporary local variables, as well as for transfer parameters to the called subroutine.
- The R5 register will be used as a frame pointer.
- The R0 register will be used to return a WORD value. The combination of R0-R1 will be used to return a LONGWORD value.
- R0 and R1 can be clobbered by a called subroutine.
- The calling program will remove the parameters from the stack.
- The calleee will remove any local variables and saved registers from the stack.
# Types of control transfer
- Subroutine call (JSR)
- Synchronous trap (TRAP xx, syscall)
- Asynchronous trap (traps generated because of error conditions, or asynchronous traps generated by the operating system itself).
- Interrupts (generated by hardware)
## Subroutine calls
A subroutine call is done my means of the execution of a JSR PC,XXX instruction. The processor saves the next instruction address (the one to execute after the subroutine return) into the R6 stack and transfers control to the destination address. So at entry of the called subroutine the SP points to an empty stack cell, and at 2(SP) we can find the return address.
The GCC compiler ABI specifies that the R0 and R1 registers can be clobbered by the called subroutine, so we don't need to save those ones. R2, R3 and R3 must be preserved thru the call, so we must save them if we are going to use those in the subroutine.
The called subroutine will do the following just at entry:
- Push the current frame pointer (R5) into the stack.
- Get the current value of the stack into R5.
- Allocate any needed local variable space by subtracting from SP.
- Push the GPRs used in the subroutine (R2..R4 only).
- Push the current FP in to the stack to make it easier to clean it up at return.
 After these actions, the stack frame will have the next content:
Offset to R5 or SP	Content	Description
4(R5), 6(R5),...	<Params>	Parameters
2(R5)	PC	Return address
0(R5)	R5	Previous frame pointer
-2(R5)	n words of local variables	Automatic variable storage
-(2+2*n)(R5) | 6(SP)	R2	Saved R2
-(4+2*n)(R5) | 4(SP)	R3	Saved R3
-(6+2*n)(R5) | 2(SP)	R4	Saved R4
-(8+2*n)(R5) | (SP)	R5	Current frame pointer

Observe that n can be zero (if the subroutine does not use any local automatic variable).
The sequence of instructions to build this stack frame is this:
subroutine:	mov	r5,-(sp)	; Save previous frame pointer
mov	sp,r5	; Set up current frame pointer
sub	$2*n,sp	; Allocate space for local variables
mov	r5,-(sp)	; Push the current frame pointer
mov	r2,-(sp)	; Push the GPRs...
mov	r3,-(sp)	;
mov	r4,-(sp)	;
mov	r5,-(sp)	; Pull gain the current FP for reference

The subroutine can reference the passed parameters using positive offsets to R5, being 4(R5) the first parameter, 6(R5) the second one, and so on. The local automatic variables can be referenced using negative offsets over R5, being -2(R5) the address of the first local variable. A subroutine does not usually need to reference the previous values for R2..R4; it can, however, need to reference the previous value of R5 to access variables in the calling procedure (which is, by the way, a bad programming practice). It can be done simply refering to (R5).
Before returning control to the caller, the subroutine must clean up the stack. The code to do that is:
mov	(sp)+,r5	; Pull the current Frame Pointer
mov	-2*n-6(r5),r4	; Pull the saved GPRs,
mov	-2*n-4(r5),r3	; relative to the frame pointer
mov	-2*n-2(r5),r2
mov	r5,sp	; Cleanup local variables and saved GPRs
mov	(sp)+,r5	; Pull the previous frame pointer
rts	pc	; Return to caller

The system provides macros to generate that code in assembly language programs. The C compiler generates it by itself.
## Synchronous traps
In a synchronous trap, an user program transfers control to kernel code using the PDP-11 TRAP instruction. The transfer of control and the return to the invoker occur synchronously, so the situation is very similar to a subroutine call. The main difference is that the invoked subroutine will run in kernel mode, with kernel memory mapping and using the kernel stack instead of the user stack.
When the processor executes a TRAP xx instruction, it pushes the current PSW and the pointer to the next instruction to execute into the destination space stack. In MUXX as well and most of the existing kernels the TRAP code will execute in kernel mode, so there is no (direct) access to the user mode stack from the called trap handler. Although it is completely possible to use the origin stack to pass parameters to the trap handler, MUXX won't do it. MUXX will get the trap parameters trhu a parameter list pointed by R0 at entry of the trap/interrupt. This parameter list will begin with a word containing the number of elements of the list, and the elements themselves, each one using at least a word of memory (byte operands will be stacked into words). Both if R0 contains zero or it points to a parmlist with a zero length it will be assumed the trap function will get no parameters.
The PDP-11 TRAP and EMT instructions allow the programmer to code a number which will be stored as part of the TRAP/EMT instruction. This code is used to specify a function to be performed by the trap handler; a typical case use would be to specify which system call must be executed trhu this TRAP. To get that trap number, the handler has to examine the code and extract the number from the TRAP/EMT instruction itself.
Since we want to be able to use trap handlers written in C, MUXX will provide a basic trap handler which will build a standard stack-based parameter set. The C subroutines will get a standard stack frame at entry, so everything said for subroutine calls will apply.

Offset to R5 or SP	Content	Description
10+2*p (R5)	PSW	PSW before trap
8+2*p (R5)	PC	Trap return address
6+2*p(R5)	R5	Previous frame pointer
6(R5)	p word-size parameters in stack	Parameters
4(R5)	WORD	Trap code (from TRAP/EMT)
2(R5)	PC	Trap handler return address
0(R5)	R5	Trap handler frame pointer
-2(R5)	n words of local variables	Automatic variable storage
-(2+2*n)(R5) | 6(SP)	R2	Saved R2
-(4+2*n)(R5) | 4(SP)	R3	Saved R3
-(6+2*n)(R5) | 2(SP)	R4	Saved R4
-(8+2*n)(R5) | (SP)	R5	Trap handler frame pointer

The trap service routine prepare this frame and call the C handler:

mov	r5,-(sp)	; Push previous frame pointer
mov	sp,r5	; Set up current FP
tst	r0	; Have we got a parmlist
beq	noparms	; no, branch away
mov	(r0)+,r1	; Does the parmlist contain anything?
beq	noparms	; no, branch away
10$:	mov	(r0)+,-(sp)	; Push parameters
sob	r1,10$	;... until done
noparms:	mov	4(r5),r1	; R1 points to return address
mov	-2(r1),r1	; R1 contains the EMT/TRAP instruction
bic	$0xff00,r1	; R1 contains now the EMT/TRAP number
mov	r1,-(sp)	; … which is pushed in the stack
jsr	pc,C_handler	; Call the C trap handler
mov	r5,sp	; Clean up parameters from stack
mov	(sp)+,r5	; Get previous frame pointer
rtt	; Return from trap

As usual this code does not preserve R0 nor R1. It pushes the parameters referenced by the R0-pointed parmlist into the stack, gets the trap number and invokes the real trap handler, which will be a standard C routine with a standard call frame. Take into account the parameters will be in reversed order respect to the parmlist. That is, if the parmlist has “p” parameters, the 2(R0) will be found at 4+(2*p)(R5) in the C routine call frame, whilst 2*p(R0) will be at 4(R5).
The C routine signature must be of this form:
void C_handler(int trapno, param1, param2, ... paramn);
## Asynchronous traps
An asynchronous trap happens when the processor detects an exceptional condition which prevents the normal flow of execution. That condition can be from diverse origin: attempt to execute an inexistent operation, or an existent operation not available in the current execution mode, access to protected or unexistent memory, etc. Those traps are unexpected by the executing program, and the handling routine has to be able to resume the interrupted execution in case the exceptional condition could be corrected (for instance, allocating more memory for the interrupted task). That means that all the processor status has to be preserved and restored in case of resumed execution, including the usually not preserved R0 and R1 registers. Obviously there can not be parameters associated to an asynchronous trap, so the corresponding frame will not have any pushed ones. Nevertheless, the asynchronous trap handling routine might need access to the register values at trap time, so the address of the stack frame itself will be pushed into the stack as the only calling parameter.
Offset to R5 or SP	Content	Description
12(R5)	PSW	PSW at trap time
10(R5)	PC	Trap return address
8(R5)	R0	R0 at trap time
6(R5)	R1	R1 at trap time
4(R5)	R5	Handler frame pointer
2(R5)	PC	Return address
0(R5)	R5	Frame pointer at trap time
-2(R5)	n words of local variables	Automatic variable storage
-(2+n)(R5) | 6(SP)	R2	R2 at trap time
-(4+n)(R5) | 4(SP)	R3	R3 at trap time
-(6+n)(R5) | 2(SP)	R4	R4 at trap time
-(8+n)(R5) | (SP)	R5	Current frame pointer

The asynchronous trap handler will prepare the stack frame for the C handler, using this code:

mov	r0,-(sp)	; Push R0
mov	r1,-(sp)	; Push R1
mov	sp,-(sp)	; Push current SP...
sub	$4,(sp)	; ... and make it point to FP
jsr	pc,_c_handler	; Call C trap handler
add	$2,sp	; Toss FP in stack
mov	(sp)+,r1	; Pull R1
mov	(sp)+,r0	; Pull R0
rtt	; Trap done

The C handling routine should have the next declaration:
void cHandler(void *FP);

The cHandler routine can access the former machine state thru the FP pointer; the registers R0, R1 and R5, the PSW and the return address are at fixed (positive) offsets from FP. R2, R3 and R4 offsets depend on the storage allocated to local variables.
If the recovery procedure has to redirect the execution to a different address than the one saved in the stack it will modify directly the return address in 10(R5) so the rtt will jump to the corrected position in the code. In the same way, if it has to provide some information to the restarted process it will use R0 and R1 to do so (clobbering its contents in the process), modifying the saved values at 6(R5) and 8(R5). At most times, the trap handler will simply abort the process so it will not actually return control to the interrupted program.
## Interrupts
The interrupts are generated by the hardware and are by definition asynchronous respect to program execution. Their handling is very similar to the asynchronous traps discussed in the previous section. The stack frame structure will be exactly the same, and the declaration for the C handling routine will also be identical.
# Implementation
## Assembler macros
- procentry local=n
- procexit local=n
### procentry local=n
This macro will be called at the procedure entry, and will build a stack frame reserving n words of local storage in the stack. By default it will not reserve any local space.
### procexit local=n
This macro will be used at the procedure end. It will restore the GPRs saved by procentry and will clean up the stack of local storage. Obviously the value for the local= parameter must be identical to the used in the corresponding procentry invocation, or Very Bad Things will happen.
## Optimization
Once the basic macros are developed and tested, and before the written code reaches a critical mass, the procentry/procexit macros will be enhanced with the option to specify how many GPRs must be saved in the call frame (from 0 to 3). The GPRs will be saved in ascending order from R2 to R4. To maintain compatibility with the first version, the default will be to save the three registers.